## Slide 1
3.3-5V
gnd
repeat
feedthru
mic input directly to speaker
speaker +
microphone
get close!
on-board switches rec (record)
playE (play track once)
playL (play while pressed)
p2 jumper
10K default = 10 sec record time
500K pot to play w distorted sounds
-
pins to external switches
any DIY on/off switch works
rec  vcc = record
playE  vcc = play once
playL  vcc = play while pressed
ISD1820 Recording Module
8 Ω speaker OR
piezo transducer OR bone conductor OR jack to speaker OR
DIY speaker coil

## Slide 2: audio outputs

## Slide 3
3.3-5V
GND
speaker
ISD1820 + 8 ohm speaker
any on/off switch

## Slide 4
3.3-5V
GND
bone conductor transducer
ISD1820 + bone conductor speaker
any on/off switch

## Slide 5
3.3-5V
GND
piezo transducer
ISD1820 + piezo speaker
Put between your teeth or on jawbone to hear sound
any on/off switch

## Slide 6
3.3-5V
GND
3.5 mm audio jack
ISD1820 + 3.5mm jack
Then connect to any battery powered speaker for bigger sound
any on/off switch

## Slide 7: amplifier

## Slide 8
shared GND!
any 4-32 ohm speaker
amplifier for louder sound: Velleman PMK190’1 + ISD1820
any on/off switch
6 - 14V
3.3-5V
3.5mm mono jack

## Slide 9: distortion

## Slide 10
3.3-5V
GND
speaker (or other output device)
ISD1820 + 500k pot
on p2: distorts the sound
any on/off switch
250K or 500K potentiometer
Ω | Record time | Sample rate | Bandwidth
80K | 8 secs | 8 KHz | 3.4 KHz
100K | 10 secs | 6.4 KHz | 2.6 KHz
120K | 12 secs | 5.4 KHz | 2.3 KHz
160K | 16 secs | 4.0 KHz | 1.7 KHz
200K | 20 secs | 3.2KHz | 1.3 KHz
default when jumper is used

## Slide 11
3.3-5V
GND
speaker (or other output device)
DIY variable resistor
make with conductive paint
any on/off switch
Ω | Record time | Sample rate | Bandwidth
80K | 8 secs | 8 KHz | 3.4 KHz
100K | 10 secs | 6.4 KHz | 2.6 KHz
120K | 12 secs | 5.4 KHz | 2.3 KHz
160K | 16 secs | 4.0 KHz | 1.7 KHz
200K | 20 secs | 3.2KHz | 1.3 KHz
default when jumper is used
0 Ω 50K Ω 100K Ω 200K Ω

## Slide 12: triggers

## Slide 13
3.3-5V
GND
speaker (or other output device)
ISD1820 + light sensor
any on/off switch

## Slide 14
3.3-5V
GND
speaker (or other output device)
ISD1820 + light sensor
conductive material
conductive material

## Slide 15
3.3-5V
GND
speaker (or other output device)
ISD1820 + Piezo transducer
Press, bend or knock trigger

## Slide 16
3.3-5V
GND
speaker (or other output device)
ISD1820 + DC motor
Type e.g. 4.5-15V with gearbox

## Slide 17
3.3-5V
GND
speaker (or other output device)
sensitivity pot
ISD1820 + light sensor

## Slide 18
3.3-5V
GND
speaker (or other output device)
ISD1820 + tilt switch
also useful as record switch!
sensitivity pot

## Slide 19
3.3-5V
GND
speaker (or other output device)
ISD1820 + red laser sensor
sensor eye

## Slide 20
3.3-5V
GND
speaker (or other output device)
ISD1820 + vibration sensor
sensitivity pot

## Slide 21
3.3-5V
GND
speaker (or other output device)
ISD1820 + hall effect sensor
magnet

## Slide 22
3.3-5V
GND
speaker (or other output device)
ISD1820 + reed switch
magnet
sensitivity pot

## Slide 23
3.3-5V
GND
speaker (or other output device)
ISD1820 + motion sensor
Needs min 4.5V (might not be reliable at 3.3V)
Tx pot to adjust delay of trigger
Sx pot to adjust sensitivity (distance)